## Slide 1
VPL: A Novel Cost Model for Earth and Mars-Orbit Navigation and Communication Constellations
M. Cholevas (TU München) • G. Vardanikas (TU Delft)
ESA/CNES Cost Engineering Conference 2026
The problem
Limited public unit-cost data for navigation and communication constellations. Legacy models (SMAD USCM8, QuickCost) rest on data up to the early 2000s. We build a cost model on 25 systems (1997–2025), that also covers New-Space systems.
The resolved CER model
TOTAL(M,N) = F·g·[ DEV(M) + PFM(M)·N^LRE ]
DEV(M) = 5.99·M^0.613 PFM(M) = 0.219·M^0.828
M = platform mass [kg], N = units, cost in FY2025 €M.
LRE = 1 + ln(0.9)/ln(2) = 0.848
g = 1 traditional, 0.120 New-Space. F = 1 Earth, 1.14 Mars.
Plug in M and N → programme cost.
Main metrics
0.94 cross-validated R²
5–21× New-Space cheaper
≈ USCM8+QuickCost on traditional;
but SMAD over-predicts New-Space ~7×
Cost-Plus vs New-Space Economy
New-Space mass-produced builds are 5–21× cheaper per kg than traditional cost-plus bespoke systems.
Validation
Leave-one-out cross-validation over 25 systems. The CER tracks unit cost across three orders of magnitude (R² = 0.94 pooled, 0.85 traditional-only).
Development vs production
The DEV/PFM split is fixed by disclosed programme budgets (US SARs, ESA), not by the fit.
Cost vs mass and constellation size
Iso-cost contours of TOTAL(M,N). VPL Traditional tracks the SMAD benchmark, with VPL New-Space a full band below.
Planetary cost factor
A subsystem bottom-up estimate gives a Mars bus-cost increase of 10% ± 4.5%, adopted as F = 1.14 (Earth F = 1). This replaces SMAD/QuickCost's blanket 1.29 planetary factor. Sources: RAND TR-418; Jones (ICES 2015).
Operations
Mission operations use the SME-SMAD Table 11-28 model: €159 M for 31 satellites over 5 years. Drivers: flight and ground software maintenance (SLOC), 19 engineers + 4 technicians, facilities and ground-hardware maintenance.
Data and code
GitHub repository with the dataset, per-number sources, the Python model, the reproduction notebook, this poster and a detailed report.
github.com/cholevasm/vpl-cost-model